## Slide 1: Spatially dense air pollutant sampling: Implications of spatial variability on the representativeness of stationary air pollutant monitors
Hugh Li1, Peishi Gu1, Qing Ye1, Naomi Zimmerman1, Ellis Robinson1, R. Subramanian1, Joshua Apte2, Allen Robinson1, Albert A. Presto1
1Center for Atmospheric Particle Studies, Carnegie Mellon University, Pittsburgh, PA 15213
2Department of Civil, Architectural and Environmental Engineering, The University of Texas at Austin, Austin TX 78712

## Slide 2: Objective
Spatial variation of NO2, UFP, and PM1
Modifiable factors to describe pollutants’ spatial variation
Spatial representativeness of monitors in a variety of neighborhoods

## Slide 3: Airborne gas and particle pollutants
Nitrogen dioxide (NO2)
EPA.gov
Notes: they are tiny;
EPA set standards for them

## Slide 4: Ultrafine particles (UFP, Da < 0.1 µm) found inside brain
Maher et al., PNAS 2016
Environment-assured.com
Notes: Ultrafine a new interest, it’s the fraction xxx;
Small size, penetrate through cell membranes, body organs
Transmission electron microscopy

## Slide 5: Do regulatory monitors represent air pollution in their surrounding areas well?
Apte et al., EST 2017
4 km
Notes: They are toxic and here comes another problem, variable;
Here I am showing you the spatial variation of BC, NO, NO2 with mobile sampling using google street view vehicle;
Say here monitors might not represent areas far away

## Slide 6: In CTM and remote sensing research, is it fair to assume regulatory monitors can represent a whole modeling grid (~km2)?
Notes: In other words, can we quantity the uncertainty?

## Slide 7: Center for Air, Climate and Energy Solutions
Mobile sampling
Supersite
Stationary monitors

## Slide 8: Mobile sampling around stationary monitors
Li et al., Submitted 2018

## Slide 9: Instruments on mobile and stationary monitors
Mobile
NO2 (T200, Teledyne)
UFP (Fast Mobility Particle Sizer 3091, TSI)
PM1 (Aerosol Mass Spectrometer, Aerodyne)
Stationary Monitor
NO2 (SenSevere Real-time Affordable Multi-Pollutant monitor)
PN (CPC, Aerosol Devices)
PM2.5 (Neighborhood Monitor, Met One)
Notes: Ramp: Electrochemical sensors
PM1 from AMS also includes BC

## Slide 10: Both mobile and stationary sampling describe similar pollutant gradient

## Slide 11: Downtown area 2 shows hyperlocal (~50 m) spatial variation
Notes: NO2 regional background 7 ppb
Median enhancement, so less outlier effect

## Slide 12: In urban areas, using one monitor to represent surrounding neighborhoods introduces errors for NO2
12

## Slide 13: UFP is highly variable both spatially and temporally
Notes: Grey boxes 1800/6200 = 30% of regional background

## Slide 14: UFP spatial variation correlates with traffic and restaurant density
Notes: Site 1 missing due to instrument vibration issue
This one describes the CTM issue

## Slide 15: The reference cell statistically represents 60% of the 1 km2 driving domain
Notes: Nonparametric Wilcoxon rank-sum test

## Slide 16: Urban monitors less spatially representative than suburb ones for UFP
Notes: Y statistical not significant (similar) cells
But for PM, they both ok

## Slide 17: Conclusion
NO2 shows within-neighborhood (~1 km2) spatial variation, hotspots elevated ~5X regional background.
Spatial differences between stationary monitors and nearby UFP can be 2.5X regional background.
Spatial variability of NO2 and UFP has moderate correlation (R2 > 0.5) with modifiable factors like restaurant and traffic.
Urban monitors represent less spatial extent of their surroundings compared to suburbs ones for NO2 and UFP.

## Slide 18
Thanks for your attention!
Prof. Albert A. Presto
Center for Atmospheric Particle Studies (CAPS)
Carnegie Mellon University, PA
apresto@andrew.cmu.edu
Photo courtesy of Xiang Li
RD83587301

## Slide 19: NO2 at urban areas more variable than suburbs
Notes: Change color (urban) vs. suburbs

## Slide 20: Secondary PM1 worse correlation with traffic and restaurant

## Slide 21: CDF of hour-to-hour UFP variation based on stationary monitors
Red: 50% range
Black: 75% range